Network Databases
1. Adjacency List – A Key/Value (Node ID/List of Neighbor Node Ids) pair list containing all currently connected nodes in the local network.
2. Packet List – A Key/Value (Node ID, Edge ID/List of Packet Types w/ Sequence #’s pairs) pair list containing every packet types sequence number (When MAX_SEQUENCE is reached timeout is set to allow new packets to be broadcast immediately)
3. Routing Table - A Key/Value (Destination Node ID, Next Node ID) pair list containing the next node hop to deliver the message to (If itself then deliver to the receiving port)
Graph Operations → Update, Delete, Add

Common Header (4 Bytes Wide)
LSC Version	Routing Option	Packet Type	Origin Port Number
Source Address		Length
ROUTING HEADER (Details Below)
PACKET HEADER (Details Below)

LSC Version -
Packet Type – HELLO [Only used on connection, UNICAST ONLY W/ NEIGHBOR], DBD (Database Description) [Packet containing the, UNICAST ONLY W/ NEIGHBOR], LSR, LSU, LSAck
Routing Option – Unicast [No sequence is checked immediately routed], Broadcast [Sequence is checked], Multicast [Allow for Group ID’s], Anycast [Pick closest member of Group ID], Geocast [Allow for Global ID’s]

Notes: When a packet is received the broadcast option is first checked and if required the lsa header is also checked.

LSC (Packet) Header (General Overview)
LSC Version	Packet Type	Routing Option	Port Number
Source Address		Edge Address (0 → Indicates Vertex)

HELLO (Packet) Header
Packet Window Size	Keep Alive Interval Sec.	Refresh Interval Min.	Connection Options
Number of GID’s	Number of GlobID’s	EXTENDED OPTIONS
NO DATA

UPD (Packet) Header
Options	0	0	0	0	0	I	M	C	# of Source ID’s/LSU Sequence # Pairs
Source ID/LSU Sequence Number (Each pair is 6 bytes → 2 Bytes/4 Bytes)

LSR (Packet) Header
Request Options	Number of Needed LSUs
Source ID of required LSU (Takes 2 bytes per Source ID)

LSU (Packet) Header
LSU Options	Connection Options	EXTENDED CONNECTION OPTIONS
Number of Connections	Number of GID’s	Number of GlobID’s	EXT. LSU OPTIONS
DATA (Neighbors ID’s/Edge Weight (ms) - 2 Bytes per ID/2 Bytes per Weight)

LSA (Packet) Header
LSA Options		Packet Type
Source Address	PADDING
Sequence Number
NO DATA

DATA (Packet) Header
Options	0	0	0	0	0	0	I	M	# of Bytes in Packet
DATA

Routing Header (General Overview)
Window Number (2 Bits)		Start Sequence Number (30 Bits)
Window Number (2 Bits)		End Sequence Number (30 Bits)
Destination Port #

If start sequence != end sequence, store each packet into a list until every packet is received than update or fail and update if more than 3 seconds is up from last received packet for group. Depending on routing type group/global/destination ID may be present or may have common routing header and variable subpart with padding. If length of single transmission is greater than 2^30 (Overflow to value greater than a single sequence window), accept all expected packets and then upon next window add to current list (this would require a single transmission of 2^(30+POWER OF MAX PACKET LENGTH).
Unicast Header
Window Number (2 Bits)	Start Sequence Number (30 Bits)
Window Number (2 Bits)	End Sequence Number (30 Bits)
Destination Address		Destination Port #	PADDING

Broadcast Header
Window Number (2 Bits)		Start Sequence Number (30 Bits)
Window Number (2 Bits)		End Sequence Number (30 Bits)
Destination Port #	PADDING

Multicast Header
Window Number (2 Bits)		Start Sequence Number (30 Bits)
Window Number (2 Bits)		End Sequence Number (30 Bits)
Group ID #	Destination Port #		PADDING

Anycast Header
Window Number (2 Bits)	Start Sequence Number (30 Bits)
Window Number (2 Bits)	End Sequence Number (30 Bits)
Destination Address		Destination Port #	Group ID #

Geocast Header
Window Number (2 Bits)		Start Sequence Number (30 Bits)
Window Number (2 Bits)		End Sequence Number (30 Bits)
Global ID #	Destination Port #		PADDING

Neocast Header (Routed Directly to Port 0)
Destination Address	Destination Port #	PADDING